## Slide 1: FUNCTIONAL VERIFICATION AND FAULT MODELING OF A RISC-V REGISTER FILE USING SYSTEMVERILOG
Group 9:
Zherong Yu(zryu@ucdavis.edu)
Camille Chang (tyuchang@ucdavis.edu)
Yating Chang (cyating@ucdavis.edu)
Chi-Yun (William) Wang (cywwang@ucdavis.edu)
EEC283 SQ25 ADVANCED DESIGN VERIFICATION OF DIGITAL SYSTEMS

## Slide 2: Presentation Outline
Project Introduction
RISC - V Architecture Basics
Project Goals
RTL Design
Testbench (Deterministic Inputs & Random Generation Test)
Fault Injection (Stuck-ats & bit-flips)
Regression
Conclusion

## Slide 3: Project Introduction
RISC-V Architecture:
  An open-source, modular instruction set architecture (ISA) based on the Reduced Instruction Set Computing (RISC) principles
  Allowing custom extensions without licensing fees, which enables innovation, flexibility, and cost savings across a wide range of computing applications
Register file: 32 × 32-bit general-purpose registers
Project focus:
  Design a RISC-V-compatible register file
  Verify correctness using SystemVerilog
  Analyze fault resilience with modeled hardware errors (faults injection)

## Slide 4: RISC - V Architecture Advantages
Open and Royalty-Free: No licensing fees, encouraging global adoption
Modular and Extensible: Optional standard extensions for tailoring performance (e.g., floating-point, vector, security)
Simplicity: Smaller instruction set enables efficient hardware and low power usage
Scalability: Applicable to embedded, consumer, automotive, and high-performance systems
Growing Ecosystem: Increasing support from tools, compilers (e.g., GCC, LLVM), and industry players

## Slide 5: RISC - V Architecture Expected Future Growth
Market Size: Projected to grow from $6.1B (2023) to $92.7B (2030)
Unit Shipments: Expected to rise from 1.3B units (2023) to 16.2B units (2030)
Industry Adoption:
  Automotive: 66% annual growth expected due to AI and edge computing needs
  Consumer & Industrial: Widespread use in smart devices and IoT systems
  AI and HPC: Companies like Rivos are developing RISC-V-based chips for AI workloads
Geopolitical Momentum: Asia - Pacific countries promoting RISC-V to reduce dependency on foreign IP

## Slide 6: Expected Growth

## Slide 7: Project Overview
Implement a parameterized 32×32 register file in Verilog
Enforce RISC-V constraints (e.g., x0 = 0)
Develop a SystemVerilog testbench
Deterministic and randomized testing
Measure and maximize functional coverage
Inject and analyze faults (stuck-at, bit-flip)
Regression

## Slide 8: RISC-V Reg File Constraints
32 registers, each 32 bits wide
Dual asynchronous read ports
Single synchronous write port
x0 register: hardwired to 0 (write-protected)
Parameterized design to allow scalability
SystemVerilog-based RTL implementation

## Slide 9: RTL Design
– 32×32 Storage Array
logic [WIDTH-1:0] mem [0:DEPTH-1];
– x0 Hardwired to Zero
In the always_ff block, if (waddr != 0) means writes to waddr == 0 (x0) are ignored. In the combinational reads, assign rdata = (raddr == 0) ? 32’h0 : mem[raddr] ensures any read from x0 always returns zero.
– Two Asynchronous Read Ports
– One Synchronous Write Port (Write-First)
On posedge clk, if we && waddr != 0, we perform mem[waddr] <= wdata;

## Slide 10: Testbench Structure
1) Clock generation: 10 ns period
2) Instantiate DUT + Golden Model
3) Checker: compare DUT outputs vs. Golden array
4) Directed Tests (4 corner‐case scenarios)
5) Randomized Tests (10 000 vectors)

## Slide 11: Deterministic Tests

## Slide 12: Randomized Tests
After a 200 ns delay, we launch 10 000 randomized vectors.
In each iteration:
– we = $urandom_range(0,1) selects random write‐enable.
– waddr, raddr1, raddr2 each get a random number 0..31.
– wdata is a random 32-bit value.
– We wait 10 ns so that each combination has exactly one clock cycle to propagate.

## Slide 13: Test Coverage and Results (All Possible Single-BIt)
Register x0 = 00000000_00000000_00000000_00000000 (bit 31 .. bit 0)
Register x1 = 00000000_00000000_00000000_00000000
Register x2 = ...
...
Register x31 = 00000000_00000000_00000000_00000000
=> Total Possible Faults: 32x32x2=2048
51.7%
EX: Register x15 = 00000000_00000000_00010000_00000000
↑ bit 18 (value = 1)

## Slide 14: Test Coverage and Results

## Slide 15: Test Coverage and Results (Random generation of Single-Bit stuck-at faults)
Covergroup | What It Tracks | Why It's Important
fault_cov | Fault type × register address | Ensures all stuck-at faults are tested broadly
write_cov | Write address × data pattern | Ensures variety in data stimulus per register
read_cov | Read address | Ensures every register is read and verified

## Slide 16: Test Coverage and Results (Random generation of Single-Bit stuck-at faults)
Weighted Avg = 97.04%
Weighted Avg = 94.96%
Weighted Avg = 97.56%

## Slide 17: Test Coverage and Results (Random, Single-Bit stuck-at)

## Slide 18: Test Coverage and Results (Multi-Bits stuck-at faults)
Inject faults into Bit 5, 18, and 27
Register x15 = 0x08040020 = 0000_1000_0000_0100_0000_0000_0010_0000
Weighted Avg = 99.56%

## Slide 19: Test Coverage and Results (Multi-Bits stuck-at faults)

## Slide 20: Test Coverage and Results (Single Bit-Flip Fault, Random Generation)
Possible Faults: 32x32=1024
EX: Register x15 = 0000_1000_0000_0100_0000_0000_0010_0000
↑ Toggle bit 18
=> 0000_1000_0000_0100_0100_0000_0010_0000

## Slide 21: Test Coverage and Results (Bit-Flip Fault, Random Generation)

## Slide 22: Test Coverage and Results (Bit-Flip Fault, Deterministic Inputs)

## Slide 23: Regression
Goal of Regression Testing
It supports automation; running multiple testbenches with logging and coverage reports
It is crucial in iterative design and verification flows, especially when you:
Add new fault injection mechanisms
Introduce updated assertions or covergroups
Example:
If you didn’t re-run the original testbenches like tb_regfile_bitflip.sv or tb_regfile_all.sv, you would never realize that the data written during normal operation is being unintentionally flipped.
It seems like you added a new feature, but in reality, you’ve broken the basic functionality.
This silicon could not pass to DFT, Physical , and tapout.

## Slide 24: The Concept of Regression code
1. Environment Setup
Clean and re-create the working simulation library / Create folders for logs and coverage reports
2. Compilation
Use vlog to compile RTL and TB files / Apply coverage options (like -cover sbcefx) to enable statement, branch, condition, expression, and toggle coverage
3. Simulation Execution
Use vsim -c to run simulations in command-line batch mode
4. Coverage Report Generation
Use vcover report to generate HTML reports / Use vcover merge to combine .ucdb files for summary and analysis

## Slide 25: Conclusion and future work
For regression part, we may purchase license to achieve advanced simulation software functions.
Test Type | Functional Coverage | Fault Detection Rate | Notes
Bit-Flip Fault | Low (e.g. ~33%) | High (100%) | Coverage is low because flips target random combinations, but many flips cause visible effects.
Multi-Bit Faults | High (≥97%) | High (≥97%) | Multiple bits flipped per test → more fault bins covered, higher chance of detection.
All Single-Bit Faults | Very High (100%) | Moderate (~51%) | Systematically inject all 2048 faults, but many do not propagate to outputs (masked).
Test Coverage ＆ Fault Detection Comparison Table

## Slide 26: Future work
Try multi-bit-flip faults testing, increase fault coverage
Fault Type | Per Register | Total (32 Registers)
1-bit flip | 32 | 32 x 32 = 1024 faults
2-bit flip as a group | 496 | 496 x 32 = 15,872 faults
3-bit flip as a group | 4,960 | 4960 x 32 = 158,720 faults
Subtotal | 5,488 | 176,616 faults